ISBN 978-83-927084-9-0

ISSN 1232-3071

MODERNIZED А. SMOLDYREV'S CALCULATION PROCEDURE OF HYDROTRANSPORT PARAMETERS

Oleg Vitushko1, Eugene Semenenko2, Nina Nykyforova3

1Public Stock Corporation "Shahtstroymontazh", Robocha Str. 4, Donetsk, 83029, Ukraine; vitushkoo@gmail.com

2The Polyakov Institute of Geotechnical Mechanics of National Academy of Sciences of Ukraine, 2А, Simferopolska St., Dniepropetrovsk, 49005, Ukraine, evs_igtm@mail.ru

3National Metallurgical Academy of Ukraine, 4, Gagarin Pr., Dniepropetrovsk, 49600, Ukraine, ninanik@ua.fm

Abstract. The engineering calculation procedure of hydrotransport parameters of polydisperse materials, which rests on logarithmic law for description of drag coefficient dependence on Reynolds number and may be used for analytical study of parameters and operating regimes of hydrotransport, is offered. The formulas of proposed calculation procedure don't include empirically determined coefficients and first show the multiplicative dependence of critical velocity on fine, medium and coarse fractions behaviour and this dependence must be only corrected according to ratio of parameters of particles of different fractions.

KEY WORDS: hydrotransport, polydisperse material, critical velocity, hydraulic gradient.

Coal pressurized hydrotransport is widely extended at coal producers and coal-cleaning enterprises of Ukraine. Still despite its using in these technologies for more than half of a century reliable determination of coal hydrotransport parameters namely of critical velocity and hydraulic gradient [Smoldyrev (1980), Kril (1990), Dmitriyev et al. (1991), Blyuss et al. (2006), Bulat et al. (2010)] is of current importance as long as material transportation is possible only in overcritical regimes and hydraulic gradient value determines pumping station power and water consumption of working operation. For rising of calculations reliability А. Smoldyrev's calculation procedure was modernized. This calculation procedure was picked out because of its usability and taking into account a polydispersity of transporting material [Semenenko et al. (2009)]. But the essential imperfection of this calculation procedure consists in wide variation range of empirically determined coefficients, for which choice there are no one-valued recommendations. Discovered more complicated nonlinear functional dependence of critical velocity on medium and coarse fractions characteristics allows excluding of incertitude when choosing the values of empirically determined coefficients, but it requires the ramified calculation algorithm [Semenenko et al. (2009)]. This obstacle is surmountable in verifying and estimating calculations, but it presents substantial difficulties during analytical study of operating regimes of hydrotransport systems and substantiation of slurry effective velocities and concentrations. Furthermore power law used during method preparation for description of drag coefficient dependence on Reynolds number bounds applied using of this procedure because values of exponent of power and coefficient of proportionality for it are not always mentioned in reference literature. Generally these values are well-known for new pipes fabricated of polyethylene or polyvinylchloride, but for steel pipes and for a long time used pipes fabricated of other materials the logarithmic dependence is more often in use and the coefficients corresponding to this law are mentioned in reference literature [Karasik et al. (1976), Kurganov and Fedorov (1986), Silin and Vitoshkin (1964), Silin et al. (1971)]. So elaboration of engineering calculation procedure of coal hydrotransport parameters, which rests on logarithmic law for description of drag coefficient dependence on Reynolds number and may be used for analytical study of parameters and operating regimes of hydrotransport without precision loss, is of current importance.

The well-known А. Smoldyrev's (1980) dependences allow calculation of hydrotransport parameters for polydisperse materials of the same density no more than 2650 kg/m3. He also has offered the classification of materials into fine, medium and coarse fractions and has obtained corresponding formulas for drag and critical velocity calculation for each fraction. The generalization of these formulas allowed the receipt of universal dependences, which were recommended for slurries holding polydisperse materials,

;	;		(1)

; where    ;			(2)

where  – hydrotransportation critical velocity, m/s; ,  – empirically determined coefficients (3,0 ≤≤ 3,2; 3,4 ≤≤ 5,5; 0,3 ≤≤ 3,0);  – pipeline diameter, m;  – gravitational acceleration, m/s2; , ,  – mass parts of fine (d less than 0,15 mm), medium (d more than 0,15 mm and less than 2 mm) and coarse (d more than 2 mm) fractions in transporting material;  – constrained fall velocity of medium fraction particles, m/s; S – bulk concentration of slurry, parts of unit;  – average diameter of medium fraction particles, m;  – relative average density of transporting material (material/liquid density ratio);  – generalized friction coefficient of coarse fraction particles оn pipe lower wall;  – slurry hydraulic gradient, meter of water/m;  – water hydraulic gradient, meter of water/m;  – drag coefficient;  – average discharge velocity of slurry, m/s.

The experience of using of formulas (1) and (2) brought to light the range of imprecisions, which became apparent to a greater extent when material heterogeneity was too big regarding the density and particle-size distribution. The analysis of using of these formulas shows that root cause of imprecisions is uncertainty when choosing values of empirically determined coefficients  and  as well as ungrounded use of principle of superposition of medium and coarse fractions contribution to hydrotransportation critical velocity. А. Smoldyrev's formulas, which served as a basis for generalized dependences, were meant for hydraulic gradient and critical velocity calculation when transporting the slurries holding monodisperse materials. Therefore all dependences for critical velocity calculation consisted of one item. Such form of functional dependences was in compliance with experimental investigations results as well as was proved to be true by fundamental conclusions of Kril (1990), Karasik et al. (1976), Silin and Vitoshkin (1964), Silin et al. (1971) about dependence of hydraulic gradient on velocity, which in relative coordinates was described by function of such universal form:

(3)

where  – hydraulic gradient in critical regime;  – constants depending оn the state of pipeline internal wall.

Passing on the polydisperse materials the principle of superposition of drags was assumed as a basis of hydraulic gradient calculation. This principle is generally recognized and basic in hydraulics and it doesn't break existing fundamental regularities. This allowed addition of items due to one or another size grade into formula for hydraulic gradient calculation. At the same time this principle was also applied to critical velocity calculation. The disarrangements between experimental and theoretical results were smoothed by introduction of trial coefficients  and . Such way allows valid description of dependences of critical velocity and hydraulic gradient on slurry concentration only in the case of happy choice of coefficients and only for certain sorts of polydisperse material. But in such cases when transporting material consists of particles of all size grades or when fine particles are absent in it the critical velocity must be determined according to formula (1) with two items and then the fundamental dependence (3) is broken. The first item represents critical velocity when transporting medium particles and the second item represents critical velocity when transporting coarse particles. But rigorous mathematical manipulation results in formula for calculation of hydrotransportation critical velocity of polydisperse materials that differs from formula (1). In the context of А. Smoldyrev's calculation procedure critical velocity is determined in terms of M. Velikanov principle, which may be recorded by formula

,				(4)

where  – hydraulic gradient of slurry in critical regime, meter of water/m;  – hydraulic gradient of water in critical regime, meter of water/m; K – M. Velikanov constant.

It is easy to make sure that substitution of expression (2) into formula (4) and collecting terms result in nonlinear equation in regard to critical velocity and it is impossible to solve it analytically independently on selected form of drag coefficient dependence on Reynolds number. During modernization of А. Smoldyrev's calculation procedure first was ascertained the dependence of empirically determined coefficients, which were introduced by А. Smodlyrev without recommendations for their choice, on drag coefficient. Formula for hydraulic gradient calculation has such appearance:

(5)

and in contrary to formula (2) doesn't include coefficients, which must be determined experimentally.

Application of formula (5) allows correction of dependences for critical velocity calculation in the cases of hydrotransportation of polydisperse material holding particles of all three fractions or not including fine particles. After substitution of formula (5) into formula (4) the cubic equation was obtained in regard to dimensionless group dependent on Froude number in critical regime

;						(6)

;	;	;	.

The value of single positive root of equation (6) is determined from expression [Semenenko et al. (2009)]

(7)

;	  .		(8)

As it follows from formula (7) in the case of polydisperse material, which consists of medium and coarse particles, solution of equation (6) depending on q value may be reduced to the form that corresponds to the presence of particles either only coarse () or only medium () size grades. The parameter z takes into account variation of  value owing to the presence of particles of coarse size grades when  and to the presence of particles of medium size grades when . At that the numerical analysis of dependence  shows that instead of complicated functions (8) their approximations by power functions may be applied with sufficient degree of accuracy

.						(9)

In the case under consideration equation for calculation of hydrotransportation critical velocity is  and it is necessary to know dependence of value  on average discharge velocity of slurry flow in order to solve it. The analysis of known formulas for drag coefficient calculation subject to slurry velocity shows that two types of this functional dependence are used for hydrotransport systems

;		;		,

where a, , n, m – empirically determined coefficients (a and b' for logarithmic law; m and n for power law);  – kinematic coefficient of slurry viscosity.

The substitution of power dependence into expression under consideration allows analytical receipt of formula for calculation of hydrotransportation critical velocity of polydisperse materials [Blyuss et al. (2006), Semenenko et al. (2009)] whereas using of logarithmic law results in nonlinear equation, which may be solved only by means of numerical methods [Semenenko et al. (2009)]:

;		.

Using power dependency of drag coefficient on Reynolds number such expression was obtained for critical velocity of polydisperse material hydrotransportation:

.				(10)

Exponent of power n for concrete conditions may be found in reference literature.

When using logarithmic law and taking into account an order of magnitude of Reynolds numbers in critical regime of slurry flow such power series expansion is possible:

After that nonlinear equation under consideration comes to quadratic and its solution in the final shape may be written down as

.

Taking into account dependences (9) the former expression may be re-arranged to such formula for calculation of hydrotransportation critical velocity of polydisperse materials:

;					(11)

; ; ; .

Let's notice that dependences (11) and (10) in contrast to (1) don't break the fundamental regularity (3) and don't include coefficients, which must be determined experimentally. Furthermore the formula (11) in contrast to (1) and (10) first shows the multiplicative dependence of critical velocity on fine, medium and coarse fractions behaviour and this dependence must be only corrected according to ratio of parameters of particles of different fractions. At that their own efficient is for every fraction particles:  – for fine particles;  – for medium particles;  – for coarse particles. At the expense of that formulas (5), (10) and (11) are very suitable for analytical study of critical velocity dependence to detection of extremes. This is necessary during selection of rational operating regimes of hydrotransport systems and substantiation of slurry effective velocities and concentrations.

For validity test of obtained dependences (5), (10) and (11) the well-known experimental data [Dmitriyev et al. (1991), Karasik et al. (1976), Kril (1990), Silin and Vitoshkin (1964), Silin et al. (1971)] were compared with results of calculations based on conditions of these experiments in compliance with obtained dependences and this comparison results for coal and quartz sand hydrotransportation parameters are shown at the Fig. 1, 2 and in the table 1. During the hydrotransport of coal a volume quantum of fine particles was over the range from 0,04 tо 0,08, a volume quantum of medium particles was over the range from 0,34 tо 0,53 and a volume quantum of coarse particles was over the range from 0,39 tо 0,62 in the pipelines with diameter 409 and 357 mm with slurry concentration 0,125 and 0,2. The sand slurry during the hydrotransport held 76 % of particles with the size 0,87 mm and 24 % of particles with the size more than 2 mm in the pipe with diameter 150 mm with slurry concentration 8 and 12 %.

The conclusion about possibility of formulas (5), (10) and (11) using for calculation of hydrotransportation critical velocity and hydraulic gradient with sufficient for engineering calculations accuracy follows from Table 1 and Fig. 1 and 2, since error of hydrotransportation critical velocity calculation doesn't exceed 12 %.

So suggested calculation procedure sufficiently and for certain describes dependences of critical velocity and hydraulic gradient on slurry concentration for polydisperse materials.

Table 1

Comparison of calculations results with experimental data

| During calculation of | Error of calculation (%) |
| --- | --- |
| hydrotransportation critical velocity | 11,3 |
| hydraulic gradient during hydrotransport of coal | 9,48 |
| hydraulic gradient during hydrotransport of sand | 7,47 |

Fig.1. Comparison of calculations results with experimental data relating to determination of critical velocity of coal and sand hydrotransportation

Fig. 2 Comparison of calculations results with experimental data relating to determination of hydraulic gradient during hydrotransport (left – coal, right – sand)

CONCLUSIONS

1. The elaborated formulas for hydraulic gradient and critical velocity calculation don't include coefficients, which must be determined experimentally, and so are applicable for hydrotransportation of all polydisperse materials with similar density of particles by pipes fabricated of different materials and for hydrotransport in the presence of drag reducing agents with substantial rise of accuracy of calculations.

2. Dependences for critical velocity calculation are obtained in an explicit form and so are suitable for analytical study during selection of rational operating regimes of hydrotransport systems and substantiation of slurry effective velocities and concentrations.

3. The elaborated calculation procedure first shows the multiplicative dependence of critical velocity on fine, medium and coarse fractions behaviour and for given conditions this dependence must be only corrected according to ratio of parameters of particles of different fractions.

REFERENCES

Баранов, Ю.Д.,  Блюсс, Б.А.,  Семененко, Е.В., Шурыгин, В.Д., 2006. Обоснование параметров и режимов работы систем гидротранспорта горных предприятий (Bаrаnоv Yu.D.,  Blyuss, B.А.,  Sеmеnеnkо Еu.V., Shurygin V.D., 2006. Substantiation of Parameters and Operating Regimes of Hydrotransport Systems of Delfts), Новая идеология, Днепропетровск.

Булат А.Ф., Витушко О.В., Семененко Е.В., 2010. Модели элементов гидротехнических систем горных предприятий (Bulаt А.F., Vitushkо О.V., Sеmеnеnkо Еu.V., 2010. The Models of Elements of Hydroengineering Systems of Delfts), Герда, Днепропетровск.

Дмитриев Г.П., Махарадзе Л.И., Гочиташвили Т.Ш., 1991. Напорные гидротранспортные системы (Dmitriyev G.P., Маkhаrаdzе L.I., Gоchitаshvili Т.Sh., 1991. The Pressurized Hydrotransport Systems), Недра, Москва.

Двайт Г.Б., 1983. Таблицы интегралов и другие математические формулы (Dwite G.B., 1983. The Tables of Integrals and Other Mathematical Formulas), Наука, Москва.

Карасик В.М., Асауленко И.А., Витошкин Ю.К., 1976. Интенсификация гидротранспорта продуктов и отходов обогащения горно-обогатительных комбинатов (Karasik V.М., Аsаulenkо I.А., Vitoshkin Yu.К., 1976. The Intensification of Hydrotransport of Products and Cleaning Rejects of Ore Mining and Processing Enterprises), Наукова думка, Киев.

Криль, С.И., 1990. Напорные взвесенесущие потоки (Kril С.И., 1990. The Pressurized Suspension Carrying Flows), Наукова думка, Киев.

Курганов А.М., Федоров Н.Ф., 1986. Гидравлические расчеты систем водоснабжения и водоотведения (Kurganоv А.М., Fyodоrоv N.F., 1986. The Hydraulic Calculations of Water Supply and Drain Systems), Стройиздат, Ленинград.

П 59-72, 1972. Инструкция по гидравлическому расчету систем напорного гидротранспорта грунтов (P 59-72, 1972. The Instruction for Hydraulic Calculation of Pressurized Hydrotransport Systems of Soils), Энергия, Ленинград.

Силин Н.А., Витошкин Ю.К., 1964. Гидротранспорт угля по трубам и методы его расчета (Silin Н.А., Vitoshkin Ю.К., 1964. The Coal Hydrotransport by Pipes and Methods of its Calculation), Издательство АН УССР, Киев.

Силин Н.А., Витошкин Ю.К., Карасик В.М., Очеретько В.Ф., 1971. Гидротранспорт (вопросы гидравлики) [Silin Н.А., Vitoshkin Ю.К., Karasik В.М., Оchеrеtkо V.F., 1971. The Hydrotransport (Hydraulic Problems)], Наукова думка, Киев.

Смолдырев, А.Е., 1980. Трубопроводный транспорт (Smoldyrev А.Ye., 1980. The Pipeline Transportation), Недра, Москва.

Витушко О.В., Никифорова Н.А., Семененко Е.В., 2009. Усовершенствование методики расчета гидравлического уклона пульпы при гидротранспорте отходов обогащения (Vitushkо О.V, Nykyfоrоvа N.А., Sеmеnеnkо Еu.V., 2009. The improvement of calculation procedure of pulp hydraulic gradient during hydrotransport of cleaning rejects). Горное оборудование и электромеханика, 10, 41 - 44.

Витушко О.В., Никифорова Н.А., Семененко Е.В., 2009. Усовершенствование методики расчета критической скорости при гидротранспорте отходов обогащения (Vitushkо О.V, Nykyfоrоvа N.А., Sеmеnеnkо Еu.V., 2009. The improvement of calculation procedure of critical velocity during hydrotransport of cleaning rejects). Горное оборудование и электромеханика, 11, 46 - 51.

Витушко О.В., Никифорова Н.А., Семененко Е.В., 2009. Усовершенствование метода расчета параметров гидротранспорта полидисперсных материалов (Vitushkо О.V, Nykyfоrоvа N.А., Sеmеnеnkо Еu.V., 2009. The improvement of calculation method of hydrotransport parameters of polydisperse materials). Металлургическая и горнорудная промышленность, 6, 66 - 69.